# Proposal for new features selection functionalities

'SELECTPLUS' is a collection of tools for selecting objects on vectors historically developed by Barry Rowlingson and supplemented by Carson JQ Farmer.
Since 2010, the extension has received a number of improvements and new features under the name 'SELECTPLUSFR'.

This new plugin, developed by Christophe MASSE (french Ministry of Ecology) is available here :

http://plugins.qgis.org/plugins/selectplus/

The following proposal presents some functionalities that could be implemented directly into QGIS core or in the fTools extensions.
## 1. “Attributes” tool bar
Proposal 1.1 : Add the possibility for the user to make selection on :
- Active layer (see the window control layers QGIS) or
- All layers or
- first layer ( layer "highest" in the order of layers) or
- first content selection (search for all layers and stops at the first layer that returns a selection ).
A combo list will be added with these 4 options.
Proposal 1.2 : Add two functions in the existing combo list (Select single feature, Select features by rectangle, …) :
- Select all features,
- Select features by diameters : similar to the select features by radius functionality,

Proposal 1.3 : Add a new tool called “Invert selection” which would simply select all features that are not presently selected and unselect the previously selected features.

Proposal 1.4 : Add a new tool that would allow user to choose the operator used for selection. In fact, when QGIS is only using “intersects”, SELECTPLUSFR plugin provides the possibility to choose among these other operators :

- Within
- Overlaps
- Contains
- Crosses
- Disjoint
- Equals
- Touches
- DE-9IM operator

For DE-9IM operator, the user can define the mask to be used.

## 2. “Digitizing” tool bar
Proposal 2.1 : add the “Create Drawn Objects” tool into the “digitizing” tool bar.

SELECTPLUSFR includes a “Create Drawn Objects” tool that allows user to create circles or rectangles.

The procedure is as follows :
- Click button to initialize the command ;
- Click in the map window to place the center of the circle and get the box set the properties of the circle (object proposed default).
The it is possible to :

- change the type object ;
- previewing dynamic drawing of the object ;
- move the object by changing the X and Y coordinates (or scroll button) ;
- change the attributes of the object : a circle radius or width and height for a rectangle (or scroll button) ;
- change the label associated with the object ;
- change associated with the object position (only for rectangles) ;
- switch to the current way (map window) or general control ;
- recall the X and Y coordinates of the last point raised in the map window ;
- change the selection option on the layer to achieve (interaction with toolbar) ;
- make a selection with the object (no need to create it) ;
- create object (memory layer).
## 3. Ftools
Ftools could be advantageously enriched and generalized with some of SELECTPLUSFR functionalities.

Proposal 3.1 :

The “intersect” tool from the GeoProcessing Tools could be generalized so that the user can :

- Choose to select on the active layer only, or on all layers, or on first layer (layer "highest" in the order of layers), or on first content selection (search for all layers and stops at the first layer that returns a selection).
- Perform the intersection only with selected features.
- Choose the operator among Within, Overlaps, Contains, Crosses, Disjoint, Equals, Intersects (default operator), Touches, DE-9IM operator (with the possibility to set options)
- Choose between creating a new layer, creating a memory layer or making a selection on a target layer*.

* Selection on a target layer : Selection on target requires that the active layer (which will provide the target) has at least one selection. Target selection on all layers are scanned. The active layer itself is scanned or not according to the option selection.

Proposal 3.2

SELECTPLUSFR includes functionalities to create derived features :

The ftools Geometry Tools could be generalized so that the user can :

- limit the operation to selected features
- Choose the type of creation : convex hull, convex hull on for all...
- Choose between creating a new layer or creating a memory layer

Proposal 3.3

SELECTPLUSFR includes functionalities to create circles or rectangles based on layers attributes :

This functionalities could be added to the Geometry tools.